## Slide 1: Hydrological Information System
Module – Integrated Reservoir Monitoring System

## Slide 2
Examples that refer to products are intended for illustrative purposes only, and do not imply an endorsement or recommendation of any particular product

## Slide 3: Integrated Reservoir Monitoring System
Inflow
Water level recorder in upstream of reservoir preferably at the bridge
Storage
Water level:: Shaft encoder if stilling well exists or Radar/Ultrasonic in reservoir
Spillway Outflow
Water level in the downstream of spillway in the river.
Gated Spillway: Gate sensors to monitor opening and estimate discharge
Canal Outflow
Gated Spillway: Gate sensors to monitor opening and estimate discharge
Water level in the downstream of spillway in canal
Introduction

## Slide 4: Options for Reservoirs
Need all components of reservoir water balance
  Inflow + outflow + change in Storage = 0
  If sensors are installed for 2 components, third can be estimated
  However, if all three components are not measured, the losses of reservoir (evaporation and seepage) would be counted towards underestimated inflow or overestimated outflow
Inflow Sensors
  On all tributaries contributing to inflow
Outflow Sensors
  Gate Sensors On all Gates of Spill, Canals
  or at location downstream in all canals and River outflow
Reservoir Water Level Sensor – On the Dam
Introduction

## Slide 5: Reservoir Monitoring Example 1
Inflow Sensor on Bridge Upstream
Reservoir Water Level Sensor in Stilling Well
Canal 1 Water Level radar 100 m Away from Gates
Canal 2 Water Level shaft encoder in Stilling Well

## Slide 6: Criteria for selection
Reservoir Water Level
  First option is Shaft Encoder or Ultrasonic sensor if Gauge well available
  Second option is Radar from top of Dam, down looking at suitable location upstream side
  If none is available, Bubbler on upstream side of Dam
Reservoir Monitoring - 1

## Slide 7: Reservoir Monitoring Example 1
Reservoir Water Level Sensor (Shaft Encoder) on stilling Well

## Slide 8: Criteria for selection
Inflow
  Inflow sensor on all Tributaries contributing to Reservoirs
  A location upstream of reservoir, such that water level in river is always ABOVE Full reservoir level (otherwise the station will be submerged when reservoir is full)
  Sometime the suitable location could be kilometers away, depending on size of reservoir
Reservoir Monitoring - 1

## Slide 9: Reservoir Monitoring Example 1
Reservoir Inflow Radar on Bridge

## Slide 10: Criteria for selection
Outflow
  Option 1 – Gate sensors on all canals and river outlet
    Needed on all gates
    May be suitable option if Automation of Canal gates is needed in future
    Expansive option if number of gates is high
    Can share same telemetry infrastructure of Dam level sensor as distance is short
    Can be calibrated for discharge measurements, no rating curve needed
  Option 2 – Water level sensors on all canals and River outlet
    Might need own telemetry system, as distance from Dam could be high
    Would need rating curves for all water level locations
  A combination of options, with Water level in canals and Gate sensors for spillway / river outlet
  A compromise would be needed based on number of sensors needed and number of telemetry stations needed
  If the hydropower is installed, it is possible to tap energy generation (for each turbine) from SCADA system and using rating curve of turbines, outflow may be estimated
Reservoir Monitoring - 1

## Slide 11: Reservoir Monitoring Example 1
Canal 1 Water Level radar 100 m away from Gates

## Slide 12: Reservoir Monitoring Example 1
Canal 2 Water Level Shaft Encoder on Stilling Well

## Slide 15: Reservoir Monitoring Example 2
Reservoir Water level Sensor
Outflow Gate Sensors
Reservoir Monitoring - 2