## Slide 1: Hydrological Information System
Module - Automatic Weather Station and Automatic Rain Gauge
Anish
….. Hydro-Informatics Expert
The World Bank

## Slide 2
Examples that refer to products are intended for illustrative purposes only, and do not imply an endorsement or recommendation of any particular product

## Slide 3: Introduction
What is Automatic Weather Station?
What Data does it provide?
How and where that data is useful?
  Calculation of Evaporation
    Loss from Lakes and Reservoirs
  Estimation of Evapotranspiration
    Crop water requirement estimation
  Weather forecasting
    Temperature, pressure humidity variations

## Slide 4: Module Contents
Network Design
Site Selection
Selection of Instruments
Data logger
Integration of Other Sensors in AWS
Telemetry
Installation
Sensor Specification
Costs
Operation and Maintenance

## Slide 5: Physical Location
Security
Telemetry Window
Power Options
Accessibility
Ownership of Land
Site Selection

## Slide 6: Site Security
Preferably at Manned positions
Research Stations of Agricultural Universities
Dam and Barrage Sites
Govt. Rest Houses, Circuit Houses
District / Block Headquarters
Private Property
Police Stations ?
Site Selection

## Slide 7: Examples of Good Sites for AWS
AWS in a Private Property at Madana
Site Selection

## Slide 8: Examples of Good Sites for AWS
AWS on top of Bhakra Dam
AWS in WRD Premises, Gandhinagar
Site Selection

## Slide 9: Examples of Good Sites for AWS
Site Selection
Site at Brahmani, need to reach by boat, nearest road kilometers away

## Slide 10: Examples of Good Sites for AWS
Site Selection
AWS in Anand Agricultural University Campus, Anand
ISRO AWS inside Agricultural research Station in Sampli, Gujarat

## Slide 11: Examples of Good Sites for AWS
Site Selection
AWS at WRD premises near Pune, Maharashtra

## Slide 12: Telemetry Window
Site Selection
For Satellite Telemetry, Direct Line of Site
Good Mobile Coverage for GSM based
Antennae LoS Obstructed by trees
No Problem Here!

## Slide 13: Power Options
Is Reliable AC Power available?
  2-3 Hours a day enough to Recharge battery
For Solar, is enough Sunlight Available?
What should be size of Solar Panels
What should be size of Battery?
  100 AH Battery with 40 Watt Solar Panel recommended for North India
  64 AH with 24-30 Watt Panels for Tropical Regions (Below 23 degree latitude)
  In Gujarat, 26 AH Battery with 10 W Panels also used
Internal Battery not an option for AWS
Site Selection

## Slide 14: Power Options – Himachal Region
Site Selection
40 Watt Solar Panel
100 AH Battery

## Slide 15: Power Options – Gujarat
Site Selection
26 AH Battery
With 10 Watt Solar Panels

## Slide 16: Selection of Sensor
Automatic Rain Gauge
Solar Radiation
Wind Velocity and Direction
Temperature
Humidity
Atmospheric Pressure
Evaporation
Selection of Instruments

## Slide 17: Automatic Rain gauge
Tipping Bucket Rain gauge
Dual Reed Switch to count Bucket tips
Available with or without Syphon
Selection of Instruments
Odisha
Gujarat
Maharashtra

## Slide 18: Solar Radiation
Silicon Photodiode based sensors
  Calibration depends on Solar Azimuth angle
  Cheaper option
Thermopile based Sensors
  Class 1 Equipment
  Expensive but more reliable option
Selection of Instruments
Silicon Photodiode Sensor
Thermopile based Pyrometer

## Slide 19: Wind Velocity and Direction
Ultrasonic Sensor with no moving parts
  Maintenance free but expensive option
  One sensor provides direction and velocity
Selection of Instruments
Site in Gandhinagar, Gujarat
Site in Brahmani, Himachal Pradesh

## Slide 20: Wind Velocity and Direction
Wind vane and Cup Anemometer
  Cheaper option
  Moving Parts, Needs frequent maintenance
Selection of Instruments
Site in Anand, Gujarat

## Slide 21: Temperature and Humidity Sensor
Resistance based Temperature Sensor
Capacitive Humidity Sensor
Often Temperature and Humidity sensors come as single hardware
Selection of Instruments

## Slide 22: Atmospheric Pressure
Sensor based on MEMS
Indoor unit
Selection of Instruments
Site in Sampli, Gujarat
Site in Bhubaneswar, Odisha
Site in Harsar, Himachal Pradesh

## Slide 23: General Features
Central and Most Important part of AWS
Functions
  Supplies Power to Sensors,
  Reads and record data
  Pass on data to telemetry unit for transmission
  Highly configurable based on requirements
  Some Models available with inbuilt GSM transmitter
  Some Data loggers are integral part of Sensor
Data Logger

## Slide 24: Data Logger Specifications
Sensor Interface
  8 analogue channels
  8 digital input/output channels, 2 input for rain gauge impulses, 6 bidirectional
  Minimum 1 serial port for digital input SDI-12
Input/output interfaces
  One for the INSAT radio
  One for the addition of GSM radio
  One Serial Port (RS232) for communication with Laptop or programming
  USB Stick option for Data transfer
Data Logger

## Slide 25: Data Logger Specifications
Flash memory minimum 32 mb
Non-volatile flash memory
A/D resolution ≥16 bit
Individual recording intervals for each sensor/parameter
Multi-tasking operating system - must log data and transmit at same time
Digital Display for viewing current data and setting values
Power supply 12V DC, low current drain (quiescent ≤10.0mA)
Monitoring of battery voltage level
internal battery backup for clock
Data Logger

## Slide 26: Data Logger Specifications
Software
  Windows software for system configuration / communication
  English language version
  All required licenses included
  Different user levels, system of user rights / passwords, access restricted to authorized personnel
Data Logger

## Slide 27: Data logger - Examples
Data Logger
Nanjing Datalogger with Customized display for Water level and Rain; Bhubaneswar

## Slide 28: Data logger - Examples
Data Logger
Komoline Data logger with inbuilt GSM Transmitter, Ahmedabad

## Slide 29: Data logger - Examples
Data Logger
Data logger as part of Shaft Encoder with internal battery, Gandhi Nagar, Gujarat
Installed in 2001, Still working Perfect!

## Slide 30: Data logger - Examples
Data Logger
Jinyang Data logger showing input, output and communication ports, Kapla, Himachal Pradesh

## Slide 31: Data logger - Examples
Data Logger
Sutron Data Logger with in built Satellite Transmitter
Sutron Data Logger with inbuilt Satellite Transmitter, Display and Keypad

## Slide 32: Integration of AWS with other Sensors
Data Logger is the major deciding factor for feasibility of integration
With Specifications of Data Logger mentioned above, it is possible to integrate any type of station and large number of sensors
Future Integration needs should be considered for deciding Data logger Specifications
  If no need for integration – Low end Data logger
  If chance of adding more sensors in future – High end Data logger (Expansive option)
Integration

## Slide 33: Integration Examples
Integration
AWS Installed at Nangal Dam (Punjab) along with
  Reservoir Water Level
  Outflow Canal Water Level
  Connectivity via wires for Dam level and Canal A
  Wireless connectivity with Canal B

## Slide 34: Integration Examples
Integration
Integration at Bhuntar on Beas River with
  River Gauge site using bubbler
  River Discharge site using ADCP

## Slide 35: Integration Examples
Integration at Anand, Gujarat with
  Soil Moisture Probe
  Leaf Wetness Sensor
  Groundwater Level Sensor
Integration

## Slide 36: Introduction
The telemetry Device transmits data to central server location
Can provide One-Way or Two Way Communication
  One Way – Push method
  Two Way – Push and Pull Method
The communication medium can be:
  GSM Towers
  Satellites
    INSAT Radio Transmitter
    VSAT
Telemetry

## Slide 37: GSM Based Telemetry
The Telemetry device has SIM card
  Can transmit via SMS or GPRS internet
Telemetry Device can be:
Telemetry
Integral part of Data logger
Separate Device

## Slide 38: Satellite Based Telemetry
VSAT based two way communication
Telemetry
INSAT based one way communication
Finer Details of Telemetry are covered in Telemetry Module

## Slide 39: Masts
Masts should be Sturdy, rust proof
Installed on good concrete foundation
Should not vibrate with wind
Installation

## Slide 40: Solar Panels
Installation
What is wrong here?
Solar Panel in Shadow of Trees

## Slide 41: Solar Panels
Installation
Chitkul, Himachal Pradesh
Anand, Gujarat

## Slide 42: Solar Panel
Installation
What is major difference in solar Panel Installation?
Almost Horizontal in Gujarat
Almost Vertical in Himachal
What should be Right Direction?

## Slide 43: Solar Panel - Direction
In Northern Hemisphere, Solar Panel always faces South
This maximizes sunlight, specially during winter
The tilt angle w.r.t. ground should be equal to Latitude of Location
  Horizontal (0 degree tilt) at Equator
  30-35 degree for northern states
Installation

## Slide 44: Connections and Wires
Installation
Label the Connection wires if feasible

## Slide 45: General Specifications
Ambient Site Condition
  Humidity Range – 5 to 100%
  Temperature Range –
    -20 to +60 Degree for plain areas
    -40 to +40 Degree for Himalayan Regions
  Altitude –
    300 to 3000 meter for Himalayan Regions
    0 to 1000 meter for other regions
Enclosures – Outdoor Antirust and dust-free
Protection - NEMA 4 or IP65
Specifications

## Slide 46: Enclosures
Specifications

## Slide 47: General Specifications
Radiation shield of double wall
All connections and wires should be concealed
Lightning protection – All equipment to be surge protected
Fencing – Chain link fence with barbed wire
All Accessories, tools, fixtures required for installation and operation
Specifications

## Slide 48: General Specifications
User Manuals – Complete manuals in English
Operation and Maintenance manuals
  Complete Manuals including Wiring Diagrams
  System Block Diagrams
Power Consumption
  Low Power consumption with standby option
GPS for time synchronization
Power Supply – Enough to last for 6 days of operation without charging
Specifications

## Slide 49: Automatic Rain gauge
Sensor Type Tipping Bucket with reed switch
Range 0-500 mm/h
Bucket Capacity 0.2, 0.5 or 1.0 mm
  The size depends on Peak Rainfall Intensity
Specifications
0.2 mm
0.5 mm
1.0 mm

## Slide 50: Automatic Rain gauge
Accuracy (Intensity) 2 % or better
Output Interface As specified in Data logger
Rain collector Material
  Corrosion Resistance Metal (Stainless steel/ Aluminum) or UV Stabilized Fiber Plastic
Enclosure IP65
All openings of the rain gauge shall be covered with a screen to protect against insects
Syphon system to eliminate over accumulation or under accumulation of precipitation
collecting funnel diameter 200mm
Ability to service tipping buckets without involving the re-levelling of the gauge
Specifications

## Slide 51: Automatic Rain gauge
Specifications
Raingauge with UV Stabilized Fibre Plastic Body
Raingauge with Stainless Steel Body
Leveling Mechanism

## Slide 52: Solar Radiation Sensor Option 1
Sensor Type Silicon Photovoltaic
Spectral Range 400-3000 nm
Range 0-2000 W/m2
Resolution 1 W/m2
Accuracy
  5% Including Temperature Compensation
Response time 10 Sec or better
Output Interface
  As specified in Data logger
Specifications

## Slide 53: Solar Radiation Sensor Option 2
Sensor Type
  Pyranometer (CMP 11 or better)
ISO Classification ISO Class I
Spectral Range 300-3000 nm
Range 0-2000 W/m2
Resolution 1 W/m2
Accuracy
  3% Including Temp Compensation
Response time 10 Sec or better
Output Interface
  As specified in Data logger
Specifications

## Slide 54: Wind Velocity and Direction Option - 1
Sensor Type
  Ultrasonic sensor (No moving Parts)
Range
  65m/s for speed
  0–360 degrees for direction
Resolution
  0.01 m/s for speed
  0.1 degree for direction
Accuracy
  0.2m/s or 3% for speed
  +/- 2 degrees for direction
Output Interface
  As specified in Data logger
Specifications

## Slide 55: Wind Velocity and Direction Option - 2
Sensor Type
  Non Contact encoders with cup anemometer and wind vane
Range
  0.3 to 65m/s for speed
  0–360 degrees for direction
Resolution
  0.01 m/s for speed
  0.1 degree for direction
Accuracy
  0. 4 m/s for speed
  +/- 5 degrees for direction
Output Interface
  As specified in Data logger
Specifications

## Slide 56: Temperature Sensor
Sensor Type
  Resistance type Temperature Sensor
Range
  -40 to60 Degree C
Resolution
  ± 0.1°C
Accuracy
  0.3°C or better
Output Interface
  As specified in Data logger
Specifications

## Slide 57: Humidity Sensor
Sensor Type
  Capacitive/ Solid State Humidity Sensor
Range
  5 to 100 %
Resolution
  0.5%
Accuracy
  ±3% or better
Output Interface
  As specified in Data logger
Specifications

## Slide 58: Atmospheric Pressure Sensor
Sensor Type
  Temperature Compensated
Range
  800-1200 hPa
Resolution
  ±0.01hPa
Accuracy
  ±0.5 hPa
Output Interface
  As specified in Data logger
Specifications

## Slide 59
Thank You