## Slide 1
Surface-Water Instrumentation
Module 15
Some slides taken from HP-2 training module by Mark Heggli
Revised by: Steve Lipscomb

## Slide 2
Examples that refer to products are intended for illustrative purposes only, and do not imply an endorsement or recommendation of any particular product

## Slide 3: Instrumentation Solutions For:
Surface Water Level
Discharge
Ground Water
Data Loggers

## Slide 4: Surface Water Level:
Two categories of water level sensors
  Contact and Non-Contact Solutions
Contact
  Sensor or other components that are in contact with the water being measured
  Susceptible to debris, siltation, vandalism
  Includes:
    Shaft Encoder/ Stilling Well
    Bubbler
    Submersible Pressure Transducer
Non- Contact
  Sensor components are not in contact with the water being measured
  Includes:
    Ultrasonic Sensor
    Radar

## Slide 5: Stilling Well/Shaft Encoder
Concept
  Water comes into the stilling well through inlet pipes from the water source
  As water level increases and decreases, a float moves up and down with the water level
  A tape attached to the float turns a wheel which is connected to the shaft on the encoder. As the wheel turns so does the shaft.
  The shaft encoder will convert the shaft rotations to an electronic signal, which will be measured by a data logger
The components of this type of gauge include:
  A stilling well
  Inlet pipes from the water
  Float and weight
  Tape
  Wheel
  Shaft encoder
Water Inlet
Float

## Slide 6
Stilling Well with Intake Cleanout
Stilling wells can be used
with other sensors.
Stilling Well Intake Flushing System

## Slide 7: Shaft Encoder Installation and Ideal Location
Installation
  The civil works for this type of station is among the most expensive, while the sensor and associated equipment is among the least expensive sensor solutions
Ideal Location
  Stable river beds where the channel does not change or migrate away from intakes
  Site with minimal sedimentation

## Slide 8: Shaft Encoder Advantages/Disadvantages
Advantages
  Low cost of equipment
  No electronic sensor calibration required, but only checked and reset to an outside staff gauge
Disadvantages
  Expensive civil works
  Requires occasional flushing to remove sediments that may have collected at the bottom of the stilling well. If left unchecked, the sediments could eventually block the inlet/outlet pipes

## Slide 9: Bubbler
Concept
  The bubbler is a stage measurement device that has a non-submersible sensor
  Also known as a gas-purge system the system allows a small quantity of air or inert gas to bleed through a pipe or tubing to an orifice in the stream
  The pressure of the gas that displaces the liquid in the orifice is then measured by a pressure transducer located in the gauge house.
Non- Submersible Pressure Transducer

## Slide 10: Bubbler Components
  Compressor
  Orifice Line
  Pressure Transducer
  Tank
  Desiccant
Bubbler
Desiccant
Air Drying System

## Slide 11: Bubbler Types and Location
Two Types
  Non- continuous
    Only turns on at a set time
      This allows water to feed back up the orifice line so the line needs to be purged and stabilized
  Continuous
    Keeps the orifice line under pressure by producing approximately 1 bubble per second
Ideal Location
  Open Channels and Reservoirs
  Stable river bed where channel does not migrate away from orifice
  Not a lot of debris or sedimentation that can cover the orifice inlet
  Great option if there is not a bridge or other structure with a direct vertical shot to the water surface.
Maharashtra Station

## Slide 12: Bubbler Advantages/Disadvantages
Advantages
  It’s a Non-Submersible Pressure Transducer
    Elimination of risk or damage of the most expensive part (pressure transducer and compressor)
    Orifice line (least expensive component) only part in the water
  Install is relatively inexpensive compared to the stilling well for the shaft encoder
Disadvantages
  Expensive compared to shaft encoder, ultrasonic sensor and submersible pressure transducer
  Not ideal for sites with migrating or shallow channel

## Slide 13: Bubbler Advantages/Disadvantages
Advantages
  Orifice tubing is inexpensive compared with data cables
  Tubing can be run hundreds of feet if necessary, from instrument shelter to the river or stream. This is useful for rivers with widths that vary greatly from the dry to wet seasons.
Disadvantages
  More mechanical parts to wear out or malfunction making maintenance more expensive and time consuming than other solutions.
  System requires more power to operate compressor. (larger solar panels, batteries, etc.)

## Slide 14: Submersible Pressure Transducer
Concept
  The pressure exerted on the sensor by the head of water above the sensor is converted to depth.
Components
  Submersible pressure transducer
  Pipe or plastic conduit

## Slide 15: Submersible Pressure Transducer Installation and Setup
Installation
  The transducer is installed in a pipe below the minimum water line
Ideal Setup
  Protected area with little possibility of debris damage or theft
  It is often used to measure water level in wells

## Slide 16: Submersible Pressure Transducer Advantages/Disadvantages
Advantages
  Relatively easy to install
    Sensor only needs to be run down a pipe to some level that is lower than the expected minimum water level
  One of the lowest cost sensors (ranging 50,000-80,000 INR)
Disadvantages
  Contact solution is in contact with the water where it is vulnerable to debris during high water flows and water pollution
  More susceptible to damage caused by vandalism or unintentional damage by animals or people.
  Any required calibration must be performed at the factory

## Slide 17: Submersible Pressure Transducer Advantages/Disadvantages
  If they prove to be reliable even after freezing they would be a good all-round choice for a water-level sensor in most applications (SW and GW)
  Cost of cable is a consideration
  A common disadvantage of pressure transducers was their vulnerability to damage if frozen. Thus they weren’t a good option for high elevation streams that are subject to ice in the winter.
  Some new products have now been developed with ceramic sensors that claim to overcome this problem.

## Slide 18: Non-Contact Solutions:
Ultrasonic Sensor
Radar

## Slide 19: Ultrasonic Sensor
Concept
  The ultrasonic sensor measures the distance of target objects (water surface) by sending pulsed ultrasound waves at the object and then measuring the time for the sound echo to return. Knowing the speed of sound, the sensor can determine the distance to the object
  Speed of sound is affected by temperature so compensation is needed
Components
  Sensor
  Mounting Platform
  Pipe

## Slide 20: Ultrasonic Sensor Installation and Location
Installation
  Requires some sort of bridge or platform to mount the sensor
  Sensor must not have any object within the area of signal projection
  Should be mounted where it can easily be accessed to repair if necessary
Ultrasonic Sensor
Signal Projection
Data Logger
SDI-12 Converter
Ultrasonic Sensor

## Slide 21: Ultrasonic Sensor Installation and Location
Ideal Location
  Need a Bridge or Platform directly over water
  Not practical in reservoirs or rivers with shallow slopes
  More ideally suited for canals
  Measurement distance up to 10m

## Slide 22: Ultrasonic Sensor Advantages/Disadvantages
Disadvantages
  Need structure to mount the sensor (bridge railing or boom)
  Measurement is not as accurate as other measurement techniques, usually being within .25 to .4 % of the measured distance
Advantages
  The advantage to the ultrasonic sensor is the price (around 75,000 INR)
  Non-contact method of measurement. The measurement is generally unaffected by the transparency, reflectivity, opacity or color of the target

## Slide 23: Radar
Concept
  The radar works by releasing electromagnetic energy, which is reflected by objects with high dielectric properties (ex: metal and water)
  The distance reflected by the microwave energy is determined by the measurement of the time of flight divided by the speed of light.
  Various frequencies from 1 Ghz to 30 Ghz are typically used, with the higher the frequency, the more accurate and more costly the device
  Components
    Radar
    Mounting Platform
    Pipe

## Slide 24: Radar Installation and Location
Installation
  Requires some sort of bridge or platform to mount the sensor
  Sensor must not have any object within the area of signal projection
  Should be mounted where it can easily be accessed to repair if necessary
Ideal Location
  Better than ultrasonic sensor for use in moist, vaporous, and dusty environments as well as in applications in which temperatures vary
  Requires some structure (bridge railing or boom) to be mounted on

## Slide 25: Radar Advantages/Disadvantages
Advantages
  Non-Contact Solution
  Radar will penetrate temperature and vapour layers that may cause problems for ultrasonic
  Compared to the ultrasonic, radar provides a solution with a greater range of detection between the sensor and the water body (> 30 m)
  The radar is more accurate than the ultrasonic sensor
Disadvantages
  Need a bridge or platform to mount (same as ultrasonic sensor)
  More expensive than ultrasonic sensor

## Slide 26: Discharge
Acoustic Doppler Systems
  Fixed mounts
  Profilers
  Other applications

## Slide 27: Acoustic Doppler Systems
Concept
  Acoustic Doppler systems rely on SONAR which uses sound waves to determine the distance to targets
  The Doppler Effect is used to resolve the velocity of flowing water by bouncing acoustic signals of a known frequency off backscatterers or targets in the water column and measuring the change in frequency of the return signal.
  Targets are generally sediment or organic materials in the water column that are moving at the same velocity and direction as the water.
Types
  Fixed
  Current Profilers

## Slide 28: Acoustic Doppler Current Profilers (ADCP)
Acoustic Doppler Velocity Meters (ADVM)

## Slide 29: ADVM - General Information
Well-suited for discharge measurements in canals with fixed channel geometry
Effective for monitoring discharge in tidally affected rivers or other unsteady flow reaches
ADVM’s can be a good alternative for streams where constant silting causes inaccuracy when using the traditional stage-discharge method.
Useful for acquiring detailed velocity data for model calibration.

## Slide 30: Upward Looking ADVM
ADVM is mounted to the bottom of the channel.
Channel shape is input into data logger for calculation of discharge.
Ideal Locations
  Canals where the water is generally free from sediment and debris
  Pipes or culverts flowing full or partially full

## Slide 31: Side Looking ADVM
ADVM is mounted on or near one of the banks of a channel.
Velocity is calculated along beam paths and converted to average channel velocity using an “Index-Velocity” rating.
The cross-sectional geometry is surveyed and used to calculate discharge.
Ideal Location
  Typically deployed in an natural channel
    Reduces the chance for sediment covering the sensor
    Sensor mounted out of the way of highest velocities and potentially damaging debris

## Slide 32: SonTek Argonaut SL
Notes: Here are photos of the most common horizontal profiler – the SonTek Argonaut SL. The photo on the right shows a SonTek ADP SL at a gauge on the Columbia River in Oregon.

## Slide 33: Nortek EZ-Q
Notes: This is a Nortek EZ-Q mounted to a bridge pier in Indiana. It was mounted to the pier ‘facing’ towards the left bank. Do you notice anything odd or wrong about the discharge measurement being made in the photo on the right?
The streamgager is standing in the area that includes the sampling volume for the horizontal profiler.

## Slide 34: Sontek Uplooker ADP
Notes: This is a photo of a SonTek ADP uplooker that was used for some work in Florida. The ADP was direct-cabled to shore.

## Slide 35: Sontek Argonaut SW
Notes: Here is one of the newer profilers, the SonTek Argonaut SW. This profiler was originally designed for use in shallow canals and can be used to directly measure the flow. It is being used in several offices in the USGS as an index-velocity meter.

## Slide 36: ADCP (Current Profiler)
Used for making instantaneous discharge measurements in lieu of standard mechanical meters using cups or propellers
Usually attached to a motorized boat or towed flotation device

## Slide 37: ADCP Discharge Measurement
Computes discharge on-the-fly
Provides complete velocity structure and channel geometry for model input

## Slide 38: High Flow - Mississippi River
Notes: Here is a high flow discharge measurement that was made at St. Louis during the 1993 Mississippi River Flood. This transect took less than 10 minutes to make and the measured discharge was > 1 million cubic feet per second. Even 4 passes (as required by OSW policy) would have only taken 30-40 minutes, not counting boat launch and retrieval. In comparison, Price AA measurements made near the gage from the Poplar Street bridge required 4-6 hours.
ADCP’s are great tools for making high flow discharge measurements and allow for significant improvement in efficiency. The Indiana District reported that they were able to make approximately 50 measurements in a 1-week period during a flood event in July 2003.

## Slide 39: Low Flow Measurements
Mean Velocity = 0.05 ft/s
Notes: This slide illustrates a discharge measurement of a very low flow – where the mean velocity was 0.05 ft/s ( xx cm/s ). This measurement was made in the Chicago River, where the cross sectional area is in excess of 4,000 square feet.

## Slide 40: Index-Velocity Ratings
Notes: ADCPs are also used to develop index velocity ratings such as the one shown here. At this site, prior to usage of the ADCP, no measurements were possible for velocities ranging from about 1.5 ft/s to 4.00 ft/s, due to the rapidly changing flow conditions and the time required to make a Price AA measurement. The measurements ranging from 2.4 to 3.2 ft/s (red dots) provided definition of the rating that was unavailable using conventional methods.

## Slide 41: Some Commonly Used ADCPs
RDI Rio Grande ADCP
SonTek ADP
SonTek Mini-ADP
RDI StreamPro
Notes: Here are some of the commonly used ADCP’s. One ADCP not shown is the Boogiedopp ADCP. The future of the Boogiedopp is somewhat ‘up in the air’ at present, although there are approximately 10 in use in the USGS.

## Slide 42: ADCP Deployment Methods
Motorboat
Tethered boat
Kayak (paddle boat)
Remote controlled boat

## Slide 43: Streamflow Measurement – Tethered Boats
Notes: This slide shows a tethered boat being used to make a discharge measurement. With tethered boats, ADCP data is radioed from the ADCP on the boat to the ADCP operator who is located somewhere on the shore (see photo on the left). Tethered boats measurements require 2 people, one to operate, configure, and collect data from the ADCP, and the other to operate the boat by means of a tether. This person can set up anywhere as long as he/she is within range of the radio modems. The other person tows the tethered boat back and forth across the measurement section (photo on the right).
What potential problems do you observe in the measurement being made on the right?

## Slide 44: Site Problems
Complex currents, turbulence, and reverse flows around bridges can result in a poor measurement section
Bridges with truss structures make it difficult to tow a boat across the channel.
Notes: Lots of turbulence downstream of piers. The left edge actually has reverse flow. Truss bridge makes it very difficult to tow the boat across the channel.

## Slide 45: Tethered Boat Measurements
Advantages:
  Less time on bridges compared to conventional bridge measurements, reducing exposure to traffic hazards
  Fast and easy deployment
  Can often be used where manned boats cannot be launched
  Can move more slowly across the river with more control than a manned boat, depending on site conditions
Disadvantages:
  Generally confined to the downstream side of bridge with limited ability to change measurement sections by changing rope length
  Turbulence from bridge piers and abutments can degrade measurement quality
Notes: Advantages:
Generally safer than using manned boats
Can be deployed easier and faster than manned boats
Can often be used where manned boats cannot be launched
Can be moved across the river more slowly and with more control than a manned boat; improving ADCP measurement quality at some sites.
Advantages of using tethered boats for ADCP measurements:
When compared to convention price AA bridge measurements, tethered boat ADCP measurements made from bridges require less time spent on bridges. This reduces the time people are exposed to traffic hazards.
Tethered boats can be quickly deployed from bridges without long setup time.
For sites where there is not a boat ramp for launching manned boats, tethered boats can be lowered from bridges, or used from cableways.
In many situations, especially in smaller streams, it can be easier to make a more controlled measurement when using a tethered boat compared to a large manned boat.

## Slide 46: Cableway Measurements

## Slide 47: Cableway Measurements
Notes: Canadian remote control cable way.

## Slide 48: Tethered from a Manned Boat
Notes: Gets ADCP away from biases and other problems caused by the manned boat (metal/compass problems, flow disturbance/boat wake problems, dampens effects of “jerky” boat pilot, less pitch and roll than on manned boat when in still water)
Potential problems…
On large rivers where there is a lot of “chop” a large stable manned boat may have less pitch/roll than a small tethered boat.
Be aware of any possible flow disturbances caused by the manned boat near the tethered boat.
Depending on the method of deployment, it may harder to control boat that are tethered to manned boats.

## Slide 49: Streamflow Measurement – Remote Control Boats
Notes: In addition to using manned and tethered boats for ADCP measurements, the USGS has invested into the development of remote-controlled (RC) boats. This remote control boat can be used where use of a manned boat is difficult or unsafe, such as insufficient clearance under bridges. It could be that in the future, as we perfect the development of RC boats and their control systems, many of our measurements will be made with RC boats. This particular boat was built under contract with OceanSciences Group. The video clip in the upper right shows an earlier prototype of this RC boat.

## Slide 50: Other Applications for Acoustics
Sediment monitoring
Bathymetric mapping

## Slide 51: Using Acoustic Backscatter as a Surrogate of Sediment Concentration
Notes: Another example of use of uplookers is from New York where an uplooker is being used to estimate suspended sediment loads on the Hudson River. Shown here is a backscatter contour plot from WinRiver. The question is, Can we use acoustic backscatter (ABS) as a surrogate for suspended sediment concentration? When one studies backscatter contour plots such as this one, it seems possible, at least qualitatively.

## Slide 52: Sediment Monitoring
Successfully used to measure instantaneous suspended sediment concentration
Instrumentation at research project comparing various surrogate methods (acoustics, turbidity, laser)

## Slide 53: Acoustic Backscatter and Velocity
Velocity
Backscatter
Notes: Here are some preliminary results showing velocity and backscatter measurements made over a number of tidal cycles. You can see the increase in backscatter that corresponds to the increase in the velocities.

## Slide 54: Bathymetric Mapping
Notes: Another example of use of uplookers is from New York where an uplooker is being used to estimate suspended sediment loads on the Hudson River. Shown here is a backscatter contour plot from WinRiver. The question is, Can we use acoustic backscatter (ABS) as a surrogate for suspended sediment concentration? When one studies backscatter contour plots such as this one, it seems possible, at least qualitatively.

## Slide 55: Bathymetric Survey for Model Grid Generation
Survey Grid
Notes: The data in the subsequent slides were collected in the area designated by the red square in the center of this map. Randal and others are looking at the interaction of flow from the Sacramento River and the Delta Cross Channel.

## Slide 56: Use of Individual Beams for Bathymetry
Two tracks
Notes: Randal’s macros allow all depths and locations for all four beams to be computed and used for make a map of the bathymetry. Here, for every ensemble, 4 beam depths were obtained. The beam depths are color coded based on the depth, with blues indicating deeper depths and yellows shallower depths.

## Slide 57: Bathymetric Map Generation
Interpolation of bed elevations to x-y-z grid
Surface
Shading of
x-y-x grid
Notes: Using 60 transects in this area, and the beam depths obtained from these measurements, a 3-D surface of the bed can be created as shown here.
Do you notice any interesting features regarding the bed?
The bathymetry from the ADCP is good enough to resolve dunes in the Sacramento River (running roughly from the top left to the bottom center of the map.

## Slide 58: Modeling 3-D velocity structure at a complex location
Notes: Randal then extracted the velocity data for those same 60 transects (over 2 tidal cycles). He imported them into a program called TecPlot and developed an algorithm for interpolating the velocity data at each location on to a regularly spaced grid. This shows an animation of the velocity field over 2 tidal cycles. The colors of the vectors correspond to the elevation (or depth) associated with each vector. Notice the exchange that takes place between the Sacramento River and the Delta Cross Channel. Notice how flow actually reverses and goes upstream and into the Delta Cross Channel.

## Slide 59: Acoustic Doppler Systems: Advantages/Disadvantages
Advantages
  Measures discharge in a wide variety of unsteady flow situations and where no stage-discharge relation exists
  Ideally suited for estuaries and canals
  Instantaneous Discharge
  Saves time over conventional measurements saving time and improving safety
  Potential application in sediment monitoring and bathymetric surveys
Disadvantages
  Complexity (requires significant and ongoing training)
  Costs are high but coming down

## Slide 60: Ground Water
Concept
  Continuous ground water levels are most commonly measured with a submersible pressure transducer
  The measured pressure is converted to water depth over the sensor and from that depth to water from the surface can be calculated

## Slide 61: Ground Water Applications
External Data Logger
  Suited towards adding additional equipment to data loggers such as rainfall, evaporation, or other hydromet measurements
Internal Data Logger
  Standalone system for just ground water level recording
  Internal batteries
  No solar panels required
  Additional features such as GPRS and water quality

## Slide 62: Ground Water Continued
Other options
  Vented cable compensates for barometric pressure changes
  Non-vented cable requires post-processing to determine water level

## Slide 63: Data Loggers
Concept
  Data loggers interrogate sensors and store data at hydromet stations
  Often coupled with telemetry devices for transmitting data from remote sites to central data management center
  Data loggers can trigger and record measurements at any set time
    This includes all digital and analog hydrological and meteorological sensors
    Other measured parameters include solar panel input and battery voltage used by technical personnel

## Slide 64: Common Features of Data Loggers
Screen to view/alter data and configure devices
Very low power consumption
Multiple communication ports for simultaneous data relay (GSM/GPRS, INSAT, VSAT)
Analog, Digital, RS-232, SDI-12 Data Inputs
Digital, RS-232 outputs
Frequency of collection/logging can be different for each sensor
Logging/Transmissions can be triggered based on a measured event

## Slide 65: Common Features of Advanced Data Loggers
Ability to switch on/off power to sensors (power saving concept)
No data loss upon power loss
Automatic start up when power is restored
Program upload feature
Can calculate and store values based on sensor inputs

## Slide 66
EXAMPLES OF DATALOGGERS
Datalogger with Touch screen
Datalogger with LCD display
Datalogger with no display
Datalogger with built-in satellite transmitter

## Slide 67
EXAMPLES OF DATALOGGERS

## Slide 68: Instrument Considerations

## Slide 69: Accuracy and Precision
  Sensor accuracy
  Resolution
  Range
  Drift
  Clock accuracy
  Response time
  QA testing (trust but verify)

## Slide 70: Technical
  Power requirements
  Input/Output connections
    Type
    Number
  Memory protection
  Surge protection
  Data storage capacity
  Data handling (fill and stop or write over)
  Software and firmware
  Programming interface (display, PC, tablet)

## Slide 71: Environmental
  Operating range for temperature and humidity
  Thermal and mechanical shock (transportation, storage, and deployment)
  Vibration
  Solar radiation
  Wind
  Sand and dust
  Ice
  Corrosion
  Build quality (internal and external)
  Regulatory compliance (frequency, signal strength, FCC approval)

## Slide 72: Operational
  Maintenance requirements
  Complexity
    Installation
    Programming
    Calibration
  Expandability

## Slide 73: Procurement
  Specifications
    Too few can result in unacceptable products
    Too many can cost more and miss a good solution.
  Warranty
  Vendor support (technical and warranty)
  Cost

## Slide 74: Resources
USGS Hydrologic Instrumentation Facility (HIF) Instrument Evaluation Program http://water.usgs.gov/hif/programs/instrumenteval/
HIF Evaluation Guidance Report http://water.usgs.gov/hif/programs/instrumenteval/HIFEvaluationGuidance.pdf
USGS Water Supply Paper 2175 http://pubs.usgs.gov/wsp/wsp2175/html/WSP2175_vol1_pdf.html
USGS Office of Surface Water memo 96.05 http://water.usgs.gov/admin/memo/SW/sw96.05.html
USGS Techniques of Water-Resources Investigations Reports (TWRI) http://pubs.usgs.gov/twri/
  Book 3 – Field Measurement of Fluvial Sediment
  Book 8 – Groundwater Instrumentation
  Book 9 – National Field Manual for the Collection of Water-Quality Data

## Slide 75: Cost Table (Approximate)
Item | Cost (USD) | Cost (INR)
Shaft Encoder | 1,000 | 60,000
Bubbler | 3,000 | 180,000
Pressure Transducer | 1,000 | 60,000
ADCP | 20,000 | 1,200,000
ADVM | 5,000 | 300,000
Ultrasonic Sensor | 1,500 | 90,000
Radar Sensor | 3,000 | 180,000
Data Logger | 2,000 | 120,000

## Slide 76: Questions/Comments?