## Slide 1: Overview of Continuous Water-Quality Monitoring
Notes: Today I’m going to be addressing topics related to continuous water quality monitoring
First describe what is meant by CWQM vs discrete monitoring

## Slide 2: Purpose of Monitoring
Define the objectives of the water quality monitoring project
  Environmental impacts of effluent
  Contaminant alerts
  Plume tracking
  Trends
Notes: Establishing the objectives of monitoring is the first step

## Slide 3: How will data be used ?
  Investigate variations in water quality
    Event
    Diurnal
    Monthly
    Seasonal
    Annual
  Evaluate loads (requires flows)
  Regulations (daily mean, max, min)
  Threshold warnings
  Development of surrogate relations

## Slide 4: Design of Monitoring Plan
Data requirements
  Period and duration
    Seasonal
    Short term
    Long-term
  Frequency of data collection
    Continuous or discrete
    15 minute, hourly, daily, monthly, etc…
  Sensor selection
Notes: Once the objectives are established the monitoring plan can be designed to achieve the intended goals

## Slide 5: Water-Quality Parameters
Common parameters measured:
  Temperature
  Specific conductance
  Salinity (based on specific conductance)
  pH
  Dissolved oxygen
  Turbidity

## Slide 6: Typical Probe Specifications
Maximum depth: 60 m
Temperature: -5 to 50o Celsius
Specific conductance: 0 to 100 mS/cm
Salinity: 0 to 80 ppt
pH: 0 – 14 pH units
Dissolved oxygen: 0 to 50 mg/L, 0 to 500 % saturation
Turbidity: 0 to 1,000 NTU

## Slide 7
YSI
Water-Quality Sensors

## Slide 8
Chlorophyll-a (algae)
Temperature and Specific Conductance
Turbidity
pH
Optical
Dissolved Oxygen

## Slide 9
Clark Cell
Dissolved Oxygen

## Slide 10: Other Sensors
Troll

## Slide 11
Hydrolab
Other Sensors

## Slide 12: Temperature
Thermistor
Resistance changes with temperature
Resistance converted to temperature using algorithm
Common unit: degrees Celsius

## Slide 13: Specific Conductance
Measure of the water’s ability to conduct electrical current
Electrodes must be submerged in water
Approximate measure of the amount of dissolved solids or ions in water
Specific conductance is conductance “normalized” to 25 degrees C
Common unit: uS/cm (microSiemens per centimeter), also umhos/cm (same units)
Notes: Current flow through electrodes and sample

## Slide 14: Salinity
Not measured directly
Computed parameter based on conductivity and temperature
Essentially measuring the amount of chloride in water
Common unit: ppt (parts per thousand)

## Slide 15: pH
Measure of acid/base characteristics
pH 7.0 = neutral
pH > 7.0 = alkaline/basic
pH < 7.0 = acidic
Measures differential of hydrogen ions (H+) inside/outside of electrode
Common unit: standard pH units

## Slide 16: Dissolved Oxygen
2 major types
  Rapid pulse Clark cell
  Optical
Common units: mg/L and % saturation

## Slide 17: Advantages of Optical Sensors
Less susceptible to FOULING
Less susceptible to CALIBRATION DRIFT
Sensors require fewer site visits
Still need routine cleaning
Notes: BASED ON OWSC TESTING
Less susceptible to fouling because no oxygen is consumed.
Less susceptible to calibration drift because there is no electrochemical reaction that causes probe behavior to change.
Still need to worry about micro environments when the probe may become isolated from the environment that we are trying to measure.
More rugged in that it is much more difficult to damage the probe by hitting it with the sensor guard or aquatic bugs from puncturing holes in the membrane.
Clark cells are dependent upon rate of O2 transfer
Optical sensors do not consume oxygen

## Slide 18: Advantages of Optical Sensors, cont.
More rugged
Greater range of operation
More accurate readings at low DO
No need for stirring
Not strongly affected by temperature
Notes: Optical Sensor:
0-50 mg/L of operational range for the optical sensor.
0-20 mg/L +-.1 mg/L or 1% of reading, whichever is greater.
20 – 50 mg/L +- 15%
Clark Cell Sensor
0-20 mg/L is 0.2 mg/L or 2%, whichever is greater.
20-50 mg/L is +- 6% of reading

## Slide 19: Turbidity
Measure of water clarity
Light is emitted, scatters off particles
Amount of light scattered at 90 degrees is measured
Common units (depends on probe):
  NTU (nephelometric turbidity units)
  FNU (formazin turbidity units)

## Slide 20: Turbidity
Detector measures how much light is scattered at 90 degrees
Light source
Sample
Detector
Photo courtesy of Sontek YSI Inc.

## Slide 21: Design of Monitoring Plan
Installation type
  Flow through
  In situ
    internal logger and power
    external logger and power
Notes: Once the objectives are established the monitoring plan can be designed to achieve the intended goals

## Slide 22: Flow through system
Water from river outlet
Notes: Slide 75

## Slide 23: Flow through
Advantages
  Secure
  Reduced fouling
  Real-time data access
Disadvantages
  Requires AC electric service
  More maintenance
  Results can be less accurate (turbidity)

## Slide 24: In situ (external logger)

## Slide 25: In situ (external logger)
Advantages
  Data are secure
  Real-time data access
  Instream monitoring often yields more accurate results
  No AC requirement permits remote sites
Disadvantages
  Sonde and probes are vulnerable to vandalism and loss
  Probes are subject to fouling and damage from debris

## Slide 26: In situ (internal logger)

## Slide 27: In situ (internal logger)
Advantages
  Remote locations possible
  Instream monitoring often yields more accurate results
  Less maintenance
Disadvantages
  Telemetry not an option
  Sonde, probes, and data are vulnerable to vandalism and loss
  Probes are subject to fouling and damage from debris

## Slide 28: Continuous Water Quality Monitoring
Advantages
Needed in rapidly changing systems
Provides better understanding of interaction between constituents
Provides better understanding of transport processes
Disadvantages
Equipment costs are greater
Operation and maintenance costs are greater
Vulnerable to damage and/or loss

## Slide 29: Relations Between Parameters DO and pH
DO and pH track together
Diurnal Pattern
Why?
Aquatic organisms produce CO2 at night combining with H20 to form H2CO3 (carbonic acid) causing pH to go down.
Notes: DO goes up during the day when biological productivity is high DO drops off at night when aquatic organisms are using DO and respiring CO2
CO2 combines with H20 to form H2CO3 or carbonic acid The increased carbonic acid causes pH to go down at night.
Thus there is a direct relation between DO and pH with a strong diurnal cycle
Collecting continuous QW data allows you to better observe these types of relations which leads to a better understanding of physical processes and the interacton of constituents

## Slide 30: Relations Between Parameters Turbidity –vs- Discharge
Notes: This slide shows the relation between turbidity and streamflow.
Turbidity is a good surrogate for suspended sediment or TSS
In a natural stream you often see a first flush of sediment during the high flows that occur after a long period of low flow. (snowmelt in ID)
After this flush the sediment concentrations are often lower even during a higher flow event.

## Slide 31: Discrete vs Continuous Monitoring
Notes: In this slide we have 4 types of data shown
Streamflow (cfs)
Suspended sediment concentration (mg/l) from discrete samples
LOADEST model results which are estimates of the sediment load based on streamflow and discrete samples
Continuous suspended sediment concentrations from an Acoustic Backscatter signal (similar to turbidity)
This illustrates the disadvantage of using only a few discrete samples, even when coupled with flow, to estimate instantaneous or even daily loads.

## Slide 32: Other Surrogate Possibilities
Continuous Parameter(s) | Surrogate Constituent
Specific Conductance | TDS, Total Nitrogen
Turbidity | Suspended Sediment, Total Phosphorous
Turbidity + Temperature | Bacteria
Relations are developed using discrete samples and linear regression
Regression model used to synthesize continuous record of target parameters that are difficult to monitor.
Parameter -vs- surrogate relations are not universal but site specific

## Slide 33: Applications
Continuous monitoring the constituent or its surrogate to aid in identifying occurrence and duration of water-quality parameters that exceed regulatory limits.

## Slide 34: Relation between SC and TN
Chart: SC (uS/cm)

## Slide 35: Applications (cont)
Identify and optimize periods for sample collection
Quantify constituent loads (volume/time)
Familiarity with the site and data will lead to a better understanding of physical processes and interactions between constituents

## Slide 36: Questions?