## Slide 1
CANAL NETWORK CONTROL
AJAY K BASU
akbasu48@gmail.com

## Slide 2: Objective
To reliably deliver water on-demand, with high flow rates to all farmers To guarantee flows requested by users.
It is necessary to maintain the level of the canal over the off-take gate.

## Slide 3: Objective
To reliably deliver water on-demand, with high flow rates to all farmers To guarantee flows requested by users.
It is necessary to maintain the level of the canal over the off-take gate.

## Slide 4: Issues
- Known or unknown leakage
- Seepage
- Unexpected weather
- Long Canal network
- Stake holders
- Human error

## Slide 5: Control Parameters
Upstream or downstream levels at the gates.
Water flow through gates, mainly at the head of the canal and secondary canals.
Water volume

## Slide 6: Controlling Elements
Gate opening
Flow can be considered as a secondary controlling element to control levels when a two level controller is used.

## Slide 7: Major disturbances
Off take flow – actual and predicted
Rain fall – actual and predicted

## Slide 8: Constraints
Maximum and minimum levels along the canal
Maximum and minimum flows
- Operating levels at the tail of the canal

## Slide 9: Modes of operation
Demand oriented
Supply oriented

## Slide 10: Modes of control
Upstream control
Downstream control

## Slide 11: Downstream Control
Control structure adjustments (gates) are based upon information from downstream (usually levels)
Downstream control transfers the downstream off take demand to the upstream water supply source (flow at the head)
Compatible with demand oriented operation
Impossible with supply oriented operation

## Slide 12: Upstream Control
Control structure adjustments (gates) are based upon information from upstream (usually levels)
Upstream control transfers the upstream water supply (or inflow) downstream to points of diversion or to the end of the canal
Compatible with supply oriented operation
Inefficient with demand oriented operation

## Slide 13: Control Logic
Directly control gate position in order to control levels
Two level control
- Compute required gate discharges in order
to control water levels
- Manipulate gate openings to obtain the
requested gate discharges

## Slide 14: Why distributed control?
Coordination between sub-systems is needed, i.e. the avoidance of upstream disturbance amplification in canals consisting of canal reaches in series
The number of reaches and gates can be high - computational limitations for a centralized system
Different section of the canal can be managed by different control centers and even by different organizations.

## Slide 15: Possible approaches
Manual
Semi-manual
Total Automation
But underlying principle is the same

## Slide 16: Possible approaches
Manual
Semi-manual
Total Automation
But underlying principle is the same

## Slide 17: Software
In any type of control, the heart of the system is the software that implements the chosen logic. Typical software components:
- Network visualization
- Network flow control
- Scheduling
- Delivery
- Compliance
- Tariff and invoicing
- Historical Data

## Slide 18: Network visualization
Provides a visual, schematic representation of the entire irrigation network so that operators have an intuitive 360 degree, high and low-level feel of total network behavior.

## Slide 19: Network visualization
On-screen visualization of network
Fast navigation through even complex networks
- Ability to view total demand and downstream usage at any point in the network
- Segment network into areas and groups for reporting, performance monitoring, user messaging or operational management

## Slide 20: Network control
Operation of the whole canal network is optimized in response to customer requirements.
Constant flows to farmers are maintained while simultaneously eliminating spills at the end of the canals.
By eliminating unnecessary spills, more water remains available in the dam or river for use at another time.

## Slide 21: Automated Delivery
Automates the scheduling of water deliveries to utilize the available capacity of the canal system
Schedules the turnout to automatically open and close the gate at the planned time, day or night.
Farmers requesting water online and receive confirmation of order

## Slide 22: Historical data
Automatic data collection from field devices and software packages
Manual data entry with remote option via web browser/mobile device Interfaces with existing SCADA systems
Should support common industry standard data formats like WaterML
- Should analyze multi-year trends
- Report to external stakeholders

## Slide 23: Standards
WaterML 2.0 is a standard information model for the representation of water observations data, with the intent of allowing the exchange of such data sets across information systems.
Through the use of existing (Open Geospatial standard (OGC), it aims at being an interoperable exchange format that may be re-used to address a range of exchange requirements.

## Slide 24: Model Predictive control logic
Based on
Current demand/supply
Predicted demand/supply

## Slide 25: Risk Management
Risk management can be applied to optimize the Irrigation Canal operation in order to consider process uncertainties.
Uses risk metrics, forecasts the water level of reaches and evaluates cost and benefit.

## Slide 26
THE END