## Slide 1
NHI: the Netherlands Hydrological Instrument
Kees Bons
Deltares

## Slide 2: Original context NHI: national policy analysis

## Slide 3: National Water Management: waterbalances …
Catchments river Rhine, Meuse
What happens within the Netherlands ?

## Slide 4
(FEM)
---------
(FDM)
(AEM)
---------
MOZART
---------
Ministry 1
Start of NHI, 10 years ago:
different approaches, different models
Ministry 2
Regional authorities

## Slide 5: Plans in 2005: joint effort ministries + institutes one national hydrological instrument NL
  Efficiency (€)
  Quality improvement, better than old national models
  International state of the art instrument
  Preferably open data and sources

## Slide 6: Advice for the new hydrological model (2006)
coupled models surface water - saturated – vadose zone
cellsize 250 m
transient (1 – 10 days)
conceptual (lumped) approach for drainage
salt intrusion included
preferably consistent with regional models

## Slide 7: So we made NHI (2006-2010): overview of models
groundwater
Modflow
(250 m, 1-10 day, 3D)
vadose zone
Metaswap
(250 m, 1-10 days, 1D)
regional surface water
Mozart
(1- 10 days)
(0,5 – 5 km2)
national surface
water
Distribution Model
nodes+lines
(10 days)

## Slide 8: Examples NHI
moisture content
lowest (mean) groundwater level
Water demand
(e.g. level control, irrigation, flushing)
National water distribution

## Slide 9: Model component 1. IMOD-MODFLOW (saturated)
Saturated zone:
625.000 cells, 250 m (~ 440 km2 )
7 layers (WQ up to 24 layers)
use of special version of MODFLOW:
(iMOD) to handle large datasets
Notes: In the Netherlands high data availability. A blessing, but also a burden on modeling projects!

## Slide 10: In Netherlands large detailed datasets are available
~16,000 boreholes
DEM 0.5m x 0.5m

## Slide 11: Geohydrological database REGIS (Geological Survey of the Netherlands: TNO)
Borehole information processed in Regiona Geological Information System

## Slide 12: iMOD: special MODFLOW version + interface (open source, free executables)
groundwater modeling of extremely large model areas
  high resolution, high performance
using binary files for faster handling of input/output (IDF, direct access)
  up- and down-scaling techniques (flexibility resolution, extent)
  fast 1-D, 2-D and 3-D visualization techniques

## Slide 13: Modelcomponent -2 MetaSWAP (unsaturated zone)
Advanced, detailed processes in soil are needed, for example:
  accurate approach of recharging ground water
  input for effect module agriculture / nature
  Input for processes water quality
Meta model of SWAP (Wageningen UR)
  Richards’ equation simplified in 2 ‘normal’ differential equations (waterbalance + continuity of pressure heads)
  Better handling (large scale) data
  Reduction calculation time
Interface : crop – land surface – groundwater table
modelled as a continuum in addition to MODFLOW:
rootzone
Subsoil
surface
groundwater table MODFLOW
vegetation

## Slide 14: Input MetaSWAP: different databases, examples:
Soil physical data
Land use characteristics
data of different authorities
combined with research results
combined with rules of thumb
Irrigation locations

## Slide 15: Output NHI a.o. calculated evapotranspiration compared to satellite data to improve model
Satellite data ETLook
(Terra + Aqua satellite)
NHI April – June 2006
(before adjustments)
Measurements
(Eddy-correlation)

## Slide 16: 3. surface water approaches by waterbalances in models for subcatchments + main surface waters
drainage
infiltration
8500 subcatchments
252 larger catchments
Water Distribution Network
(water supply)
MODFLOW
waterlevels
Within catchments (water demand)
simulation of level control, flushing, withdrawals
datasets used of a.o. regional water boards
MetaSWAP
Irrigation demand
management strategies water allocaton

## Slide 17: Example of combining regional + national data for Deltaprogramme: National Sobek Model
Original water balance model
adjusted water balance model (black)
and generated hydraulic model (red)

## Slide 18: Overview NHI: coupling groundwater- surface water
MetaSWAP
MODFLOW
head,
recharge, storage
Mozart
sprinkling
demand / allocation
drainageflux
waterlevel
Distribution
model
water demand / allocation
Hydraulic model
Notes: MODFLOW <-> metaSWAP: ONLINE phreatic groundwaterlevel <-> recharge
MODFLOW <-> MOZART: ONLINE drainage fluxes <-> water level
metaSWAP <-> MOZART: ONLINE sprinkling demand <-> sprinkling allocation
MOZART <–> DM: ONLINE water demand <-> water allocation
MODFLOW <-> DM: OFFLINE coupling drainage fluxes <-> water levels

## Slide 19: NHI after 10 years: indispensible instrument for NL
National Policy analysis (e.g. Deltaprogramme)
Stimulus for discussions within Dutch hydrological community
Free data, software, knowledge (helpdesk) for all water parties NL (www.nhi.nu)

## Slide 20
How was it done ?
Desired functionalities
Programme
Team
Implementation
Team
Implementation programme
Strategy
Team
Guiding committees
Process organization

## Slide 21: So the first years were about
Demand driven development
Joining data and merging databases
Joining financial resources
4) Generating one high quality set of connected models
5) Many users/owners - one consistent system
Then based on that one system various developments were built:

## Slide 22
Drinking Water Companies
Waterboards
Provinces
Development-1: toolbox NHI, present:
1 national + several regional models

## Slide 23: NHI as a toolbox (2015-2018) : data + software for automatically generating models on desired scale
Tools (iMOD and others)
preprocessing,,
coupling
scaling
optimization
version management
Public data, other data
Soil
Subsurface
Surface Water
Shared model data
Soil
Subsurface
Surface Water
.
Sourcecodes
MODFLOW, SEAWAT,
MetaSWAP, SWAP, etc.
SOBEK, RTC, etc
Regional model application (fit for purpose)
National model application (fit for purpose)
open data / source
flexible (fit for purpose)
reproducible
conistency regional - national
Notes: Uitgangspunten
Instrument voor NL  regionale en landelijke model(toepassing)en verbinden
Samenwerken tbv verschillende toepassingen  fexibele koppelingen en generieke inzetbaarheid van modelcodes en tools
Samenwerken tbv delen kennis op verschillende schalen  gedeelde data (‘missende’ data en schematiseringen) verzamelen/genereren en delen
Efficiënter  opbouw via modules/componenten tbv hergebruik; als het al bestaat niet zelf ontwikkelen
Samen ontwikkelen  open source en voor alle financiers vrij inzetbaar
Ambitie samebrengen (inter)nationale ontwikkelingen  kennisinstituten ontwikkelen, beheren en onderhouden
Gezamenlijk ontwikkelen  samenwerken gebruikers/financiers en ontwikkelaars

## Slide 24
07 November 2016
meteo
river discharges
Rhine, Meuse
Development-2: Real time drought modelling
forecast water supply, groundwater, moisture etc.

## Slide 25: Thank you for your attention!
The technology is here,
The knowledge is here,
The data can be here
Where there’s a WILL, there’s a WAY