## Slide 1
Building knowledge and technology through collaborative water monitoring
National Hydrology Project
International Seminar
Pune, India
Paul Wilson

## Slide 2: Agenda
Context and history
Regional Water Monitoring Partnership
Data and technology
Moving from data to information

## Slide 3: Victoria, Australia
Population 6 million
70% live in Melbourne
25% Australia’s food production ($A15 billion/ annum)
238,000 km2
(75% size of Maharashtra)

## Slide 4: Surface water use
Chart: 
| Irrigation 79% | Stock and domestic 4% | Urban and commercial 15% | Power generation 2%
 | 0.79 | 0.04 | 0.15 | 0.02
Irrigation
79%
Urban and commercial
15%
Domestic and stock
4%
Power generation
2%

## Slide 5: Gauging sites
820 gauges
542 flow
381 water quality
287 telemetered
~2,000 groundwater bores

## Slide 6: Why a partnership approach?
1990s sell-off of state hydrographic services
Loss of government knowledge of monitoring and water resource management
Increased costs
Fragmented monitoring, duplication, inconsistent methods
Data analysis disconnected from policy development and decision making

## Slide 7: Partnership structure
DELWP
Northern Co-ordinator
Southern Co-ordinator
Advisory Committee
Chairs Committee
Technical Reference Committee
Outsourced service providers
40+ partners, including:
14 water corporations (100%)
10 CMAs (100%)
40+ partners, including:
12 local councils (45%)
State and Commonwealth
40+ partners, including:

## Slide 8: Partnership structure
SRW
GMW
DELWP
MW
BoM
Service providers
Single well-specified contract
Local
Councils
CMAs
Transparent Cost Sharing - Partnership Arrangement
Co-ordinated Network
The Partnership has simplified the procurement process:

## Slide 9: Partnership approach
Co-ordinated and consistent state-wide approach
State owns the data
Uniform standards which are fit for purpose
Cost is shared between partners
Engaged partners
Extremely flexible approach
Advances in technology and increased accuracy in data collection

## Slide 10: Contracts
Outsourced data model
2 major contracts
  Field services
  Lab services
Contract is between DELWP and the service providers
Formal Agreement between DELWP and all partners
$A10 million/ year (515 million INR)
Total contract value $A80 million (4100 million INR)

## Slide 11: Data collection

## Slide 12: Data transfer
Service providers
QA/QC
DELWP
BoM
Partners
Floodzoom
DELWP
Web- and app-based, publically available
Water register
Web-based, publically available
Not publically available
Web-based, publically available
Verified data — monthly
BoM
Real-time data

## Slide 13: Maintenance and other services
Monitoring and maintenance
Extra Works (25% of total budget)
Equipment Maintenance Fund (<10% of total budget)
Flood damage – separate budget
Equipment trials (in partnership with service provider)
Regional co-ordinators
Management, billing, databases and publication of data – paid for DELWP

## Slide 14: Technology
Technical Reference Group
Real time data
Portable Automated Loggers (PALs)
Flood intelligence platform
Modums vs radio transfer
M2M communication
Drones
Endless wires and OH+S
Site runner

## Slide 15: Technology
Subscription Notification Service
Digital Transformation Development underway
  Mobile apps to show daily storage levels
  working to provide more than just figures

## Slide 16: Moving from data to information
New emphasis
  Wider scope – rock fish ramps
  Change in messaging
    Can not under take: compliance, water allocation, measure water use, modelling and reporting (daily/ weekly/ monthly/ annual), without monitoring data.
  Evidence-based decision making
  Decisions made based upon the most up-to-date data and information

## Slide 17: Benefits
Consistency and state-wide coverage
Cost sharing
Central tendering and contracting
Market power to reduce costs
Engaged partners
Evidence based decision making

## Slide 18: Thank you
Australian Water Partnership
Austrade
Liveability Victoria International