## Slide 1: Environmental flows in IWRM
Mike Acreman

## Slide 2: IWRM goals
Economically efficient water use
Assessments of supplies, sound allocation, efficient technologies
Equitable access
Appropriate institutions, users’ associations, stakeholder sharing
Environmental sustainability
water quality standards
flow standards

## Slide 3: Draft River Basin Management Act
Environmental flows
River Basin Master Plans accounting for needs of aquatic ecosystems

## Slide 4: Managing water allocation
Environmental provision
over allocation
water resource
}
}
Irrigation
Industry
Public supply
Hydro-power

## Slide 5
Paradigm change (after WWAP)
EIA
EOA

## Slide 6: Biodiversity
Nature conservation
Biodiversity (e.g. river dolphins)

## Slide 7: Water services
Wetlands & floodplains
to regulate flows and purify water
human health

## Slide 8: Local livelihoods
Fish for fisheries
Grass for cattle
Fertile soils and natural irrigation

## Slide 9: Cultural services
Family/community history
Spiritual/religious connection
Tourism
Quality of life

## Slide 10: Brisbane Declaration 2007
Environmental flows describe the quantity, timing and quality of water flows required to sustain freshwater and estuarine ecosystems and the human livelihoods and well-being that depend on these ecosystems.
Managing water at the basin scale

## Slide 11: How much water does a river need?
No single answer
Over 250 methods
Big questions
What sort of river do you want?
What are the pressures on the river?
What will the future bring?

## Slide 12: What sort of river do you want?
natural
10,000 BC
golden age
1821
when I was young

## Slide 13: Objective-based flows
Conservation objective
maintain nature character e.g. Ramsar site
Ecosystem service objective
Maintain depth for river festival

## Slide 14: Scenario-based flow setting
No pre-set objective
Stakeholder participation
– awareness raising
local community action
Trade-off between water uses
– economic value
political decision
£

## Slide 15: River management classes
Class 1 natural
Class 2 semi-natural
Class 3 working river

## Slide 16: 2012 Blueprint to Safeguard Europe's Water Resources
Pressure on river ecosystems
No 1 pressure = dams, land drainage; flood embankments
No 2 pressure = over-abstraction of water → identification of “ecological or environmental flow”
What are the pressures on the river?

## Slide 17: Why is flow important?
channel maintenance flood
floodplain connectivity
maintenance flows for spawning and dispersal
freshet trigger flows for migration
low flows for juveniles
J F M A M J J A S O N D
All aspects of the flow regime are important for some element of the river ecosystem
not enough

## Slide 18
Can we quantify the importance of flow for river health?
LIFE score
Flow index
1991
1997
2001
2009
No threshold

## Slide 19
flow
flow
flow
flow
flow
flow
Ecosystem score
Ecosystem score
Ecosystem score
Ecosystem score
Ecosystem score
Ecosystem score
sensitive rivers
low abstraction
robust rivers
high abstraction
River sensitivity

## Slide 20: How do pressures alter river flow?
Direct abstractions
Reduced baseline – maintain variability
Restrictive management
Dams/impoundments
Magnitude and variability may be reduced; magnitude may be increased
Active management

## Slide 21: Abstraction management
How much can we alter the flow regime ...?
... but maintain desired ecological condition?
Standards often developed by expert panels – i.e. synthesis of knowledge and experience

## Slide 22
Headwaters
Maximum abstractions % of natural flow
Lowland meandering
Middle reaches
High flow
Drought
Medium
flow
Low flow

## Slide 23: Impoundment releases
Heavily Modified Water Body
Target = Good Ecological Potential
Best practice
Stakeholder objectives
Dams have major control over flow regime
Release flows to meet desired ecosystem services

## Slide 24: Hydro-power issues
off take
power house
return
impacted reach
river
Hydro peaking
‘ramping’
Impacted reach

## Slide 25: E-flow releases from dams
channel maintenance flood
floodplain connectivity
maintenance flows for spawning and dispersal
freshet trigger flows for migration
low flows for juveniles
Quantity – magnitude, timing, duration, frequency
Quality – temperature, sediment

## Slide 26: E-flow release regime
environmental flow
natural flow

## Slide 27: Implementation
Need strong political will to address over-allocated rivers
Identify champions
Assess supply-side and demand-side options
Provide incentives for efficiency
Define operational rules
Set-up monitoring

## Slide 28: Adaptive management
E-flow assessments uncertain
Responses un-predicable
Circumstances change
Need to act, monitor, evaluate and adjust
Not admission of error

## Slide 29: Inter-sectoral coordination
Senegal River Basin Development Authority
Senegal, Mali, Mauritania
Managing Manatali dam
Balancing hydropower, navigation, eflows for floodplain agriculture

## Slide 30
Risk of future ecological impact from hydrological alteration

## Slide 31
Environmental flow workshop NIH Roorkee October 2013
35 river system experts
academia
government researcher
NGOs
power industry
Central Water Commission
World Bank.

## Slide 32: Workshop conclusions
India has world leading water managers
Strong history in irrigation, hydraulic engineering
Environmental flows emerging issue worldwide
India need skills in environmental flows to stay at cutting-edge

## Slide 33: Conclusions
Healthy rivers are important to Indian people
Essential to human health and quality of life
Support economic activity
Healthy rivers need environmental flows
Decide what sort of river you want
Deliver the flow required

## Slide 34
THANK YOU