## Slide 1: Hydrological Modelling of Dudhnai watershed using SWAT

## Slide 2: Introduction
Hydrological responses in the mountainous areas are not well understood due to lack of studies and complex terrain
Moreover, changing climate and land uses often affects
  Characteristics of soil erosion, floods and droughts
  Water resources management practices
Hydrological modelling is becoming increasingly important for understanding the hydrological behavior of watersheds and to attain sustainability in available water resources

## Slide 3: Introduction (Contd.)
Among many models developed recently, the Soil and Water Assessment Tool (SWAT), developed by the United States Department of Agriculture (USDA) is widely used.
SWAT can predict runoff, sediment yields and water quality under varying soils, land use and management conditions over long period of time.

## Slide 4: Objectives
To prepare input dataset for setting up SWAT Model in Dudhnai watershed.
To calibrate SWAT Model using observed discharge data in Dudhnai watershed.
To validate the model and simulate water yields in Dudhnai watershed.

## Slide 5: Materials and Methods
Fig1: Study area covering parts of Assam and Meghalaya

## Slide 6: Materials and Methods (Contd.)
Study area: Dudhnai watershed
Dudhnai River originates from the East Garo hills of Meghalaya and flows into the mighty river Brahmaputra through Goalpara district.
Has flood plain near the outlet of the watershed (about 20 % area of the watershed)
A hydrological model can understand the nature of flooding by estimating the amount of runoff received
Sl. No. | Geological parameter | Value
1 | Longitude | 90° 46’ 22” E to 90° 50’ E
2 | Latitude | 25° 52’ 58” N to 25° 59’ 20” N
3 | Catchment area (sq. km) | 439.2
4 | Elevation range (m) | 49 – 683 above MSL
Outlet: At Dudhnai bridge, a CWC gauging site

## Slide 7: Materials and Methods (Contd.)
Sl. No. | Data | Source | Details
1. | Digital Elevation Model (DEM) | SRTM | 90 m spatial resolution
2. | Soil | FAO | 1:250,00,000
3. | LULC | ORNL DAAC | 100 m spatial resolution; Year: 2005
4. | Precipitation | IMD | 0.25° x 0.25° spatial resolution; daily
5. | Weather Generator | IMD | 1° x 1° spatial resolution
6. | Discharge | CWC | Daily station data
Data used:

## Slide 8: Materials and Methods (Contd.)
DEM is called Digital Elevation Model indicates the elevation of each and every point in the watershed.
LULC is defined as the spatial presentation of different locations introducing whether an area covered with vegetation, forest, urban or residential area and so on.
Soil map is representation of the soil types over a study area.
Look up tables were prepared for LULC and soil data taking references from SWAT code and FAO soil database.

## Slide 9: Materials and Methods (Contd.)
Input and processed data set for SWAT run
DEM
Soil map
LULC

## Slide 10
Methodology adopted in the study
Materials and Methods (Contd.)

## Slide 11: Materials and Methods (Contd.)
Generation of an elevation map of the study area
Freely available DEM from SRTM with 90m resolution is loaded in ArcGIS and clipped so as to cover the watershed.
The clipped DEM is set to projected coordinate system with UTM zone 46N.
Elevation map of the study area

## Slide 12: Materials and Methods (Contd.)
Delineation of a stream network
Stream network was initially delineated in SWAT using 90 m SRTM DEM.
Upon delineation, mismatched of the stream network were observed near the flatter region of the watershed (outlet region) as compared to the real world.
This may be due to inability of the DEM to detect small change in slope in very flat regions
Other DEMs such as Cartosat (30 m), SRTM (30 m), ASTER (30 m) were employed but no improvement.
Thus, with the help of google earth, streams were digitized.
The digitized stream network was late used for stream burn-in in SWAT.

## Slide 13: Materials and Methods (Contd.)
ArcSWAT is an interface in the ArcGIS software
Watershed delineation step in SWAT

## Slide 14: Materials and Methods (Contd.)
HRU analysis
LULC and soil maps are loaded and 5 classes of slope are arranged during the Land use/Soil/Slope definition step.
HRU (Hydrological Response Unit) definition is set as of default settings.
HRU is a region covering all similar land uses, soils and slopes within a sub-basin based upon user-defined thresholds.
HRU

## Slide 15
SWAT Write Input Tables Import Weather Generator data Import precipitation data Other data such as temperature (max. & min.), solar radiation, wind speed, relative humidity were simulated by SWAT using weather generator data Finally, SWAT input files were written.
Materials and Methods (Contd.)

## Slide 16: Materials and Methods (Contd.)
SWAT Simulation
Selection of simulation period: 01-01-2003 to 31-12-2019
Warm up period: 2 years
Select output settings
Click SWAT Setup, then click Run.
After successful SWAT run, the model needs to be calibrated and validated for further investigation of the research outputs. Sensitivity analysis is done prior to calibration and validation steps, this informs about the most sensitive hydrological parameters that are responsible for unpredictable nature of a watershed hydrology.

## Slide 17: Results and Discussion
After successful completion of the SWAT Run step, several basic predictions come out at the end. These predictions/outcomes are just predicted by the SWAT model and need to be calibrated with proper observed data and relevant software (SWAT-CUP).
Parameter Name | Values
Simulation length (Years) | 15
Warm up (Years) | 2
HRUs | 714
Sub basins | 84
Output time step | Daily
Precipitation method | Measured
Watershed area (sq. Km) | 439.2
Basic SWAT input parameters

## Slide 18: Results and Discussion (Contd.)
Water Balance Ratios:
Sl. No. | Parameters | Values
1 | Streamflow/Precipitation | 0.73
2 | Baseflow/Total flow | 0.46
3 | Surface runoff/Total flow | 0.54
Average hydrological parameters (in mm)

## Slide 19: Results and Discussion (Contd.)
Precipitation regime on the watershed
Chart: Rainfall (mm)
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Annual Rainfall | 2659.1981 | 1662.0419 | 2309.7367 | 2617.9943 | 2017.089 | 2772.6957 | 1811.4338 | 1952.3729 | 2092.8595 | 2738.0724 | 3431.6395 | 2191.4419 | 2658.6862 | 1848.3743 | 2668.2857
Mean Rainfall | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281 | 2362.1281
Chart: Rainfall (mm)
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Monsoon Rainfall | 1548.6586 | 1076.5448 | 1554.4529 | 1760.7743 | 1357.7757 | 1367.4943 | 1202.3248 | 1458.8162 | 1287.9533 | 2061.9829 | 2615.8838 | 1301.0952 | 1771.3481 | 1227.3543 | 1688.779
Average Monsoon Rainfall | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825 | 1552.0825
% of Annual Rainfall | 58.2378 | 64.7724 | 67.3 | 67.2566 | 67.3136 | 49.32 | 66.3742 | 74.7202 | 61.5404 | 75.3078 | 76.2284 | 59.3717 | 66.6249 | 66.4018 | 63.2908
Yearly rainfall variation in Dudhnai watershed
Monsoon rainfall variation in Dudhnai watershed

## Slide 20: Results and Discussion (Contd.)
Chart: Rainfall (mm)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
 | 6.4099 | 17.1343 | 65.3965 | 260.3357 | 334.4641 | 493.1845 | 415.8789 | 369.3932 | 273.6259 | 117.0199 | 6.4919 | 2.7933
Chart: % departure
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
% Departure | 12.5764 | -29.6379 | -2.218 | 10.832 | -14.6071 | 17.3813 | -23.3135 | -17.3469 | -11.3994 | 15.9155 | 45.2775 | -7.226 | 12.5547 | -21.7496 | 12.9611
Percent departure of annual rainfall from normal in Dudhnai watershed
Monthly variation of precipitation in Dudhnai watershed during 2005-2019

## Slide 21
Parameter Name | t-Stat | P-Value | Rank
CN2.mgt | -19.66 | 0.000 | 1
CH_K2.rte | 18.22 | 0.000 | 2
ALPHA_BNK.rte | -6.71 | 0.000 | 3
CH_N2.rte | -1.81 | 0.071 | 4
SLSOIL.hru | 1.56 | 0.120 | 5
REVAPMN.gw | -1.28 | 0.202 | 6
GW_REVAP.gw | -1.26 | 0.207 | 7
GW_DELAY.gw | 1.21 | 0.229 | 8
SURLAG.bsn | -1.03 | 0.305 | 9
SOL_AWC(..).sol | 0.93 | 0.355 | 10
SOL_K(..).sol | 0.61 | 0.545 | 11
ESCO.hru | -0.32 | 0.749 | 12
OV_N.hru | 0.18 | 0.858 | 13
GWQMN.gw | 0.16 | 0.871 | 14
ALPHA_BF.gw | 0.10 | 0.920 | 15
Ranking of sensitivity of SWAT model parameters in Dudhnai watershed
Sensitivity analysis
Results and Discussion (Contd.)

## Slide 22: Results and Discussion (Contd.)
Evaluation Parameter | Calibration (2005-2014) | 
 | Daily | Monthly
Nash-Sutclffe Efficiency (NSE) | 0.54 | 0.70
Coefficient of Determination (R2) | 0.55 | 0.72
Coefficient of Residual Mass (CRM) | -0.1 | -0.10
Standard Error of Estimate (SEE) | 20.31 | 9.33
Percent Bias (PBIAS) | -9.7 | -
Mean Simulated (Mean Observed) | 20.93(19.08) | -
Daily and monthly statistics of SWAT model performance in the Dudhnai watershed for calibration period: 2005-2014
Evaluation Parameter | Validation (2015-2019) | 
 | Daily | Monthly
Nash-Sutclffe Efficiency (NSE) | 0.44 | 0.72
Coefficient of Determination (R2) | 0.46 | 0.74
Coefficient of Residual Mass (CRM) | -0.08 | -0.08
Standard Error of Estimate (SEE) | 24.34 | 11.15
Percent Bias (PBIAS) | -8.04 | -
Mean Simulated (Mean Observed) | 25.13(23.26) | -
Daily and monthly statistics of SWAT model performance in the Dudhnai watershed for validation period: 2015-2019
Calibration of the SWAT model was done followed by validation. Calibration provides the most accurate and favorable output based on set of numerous data provided to it. Based on the best fitted value or output, validation provides the required results and conclusions.

## Slide 23
Chart: Discharge, cumecs
Daily streamflow of observed and simulated discharge for calibration period (2005-2014)
Results and Discussion (Contd.)
Chart: Discharge, cumecs
Daily streamflow of observed and simulated discharge for validation period (2015-2019)

## Slide 24
Chart: Discharge, cumec
| 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 42248 | 42278 | 42309 | 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800
Rainfall | 9.33 | 14.8 | 44.49 | 265.45 | 409.65 | 1064.75 | 371.4 | 785.38 | 341.8 | 47.25 | 11.47 | 9.82 | 14.54 | 1.99 | 43.61 | 357.48 | 371.13 | 413.25 | 537.31 | 122.6 | 241.06 | 107.06 | 0.16 | 1.84 | 0.09 | 22.93 | 76.59 | 365.26 | 247.62 | 429.97 | 471.31 | 481.14 | 405.2 | 174.92 | 3.11 | 0.37 | 0.35 | 13.14 | 68.25 | 174.07 | 309.9 | 378.17 | 268.21 | 268.27 | 305.36 | 24.2 | 15.09 | 18.88 | 0.28 | 24.07 | 39.71 | 208.75 | 528.94 | 377.36 | 761.44 | 195.39 | 343.32 | 166.78 | 11.67 | 0.02
Qobs | 5.4673 | 3.1524 | 2.8705 | 10.6345 | 24.7624 | 55.7911 | 32.142 | 81.0167 | 81.9653 | 27.5621 | 13.0725 | 10.059 | 8.6068 | 7.239 | 6.0907 | 17.5636 | 32.3243 | 18.0679 | 53.0583 | 37.2593 | 30.3497 | 23.1537 | 8.9491 | 5.6076 | 4.2123 | 2.5364 | 4.3505 | 30.761 | 25.9038 | 40.0603 | 59.3205 | 61.4092 | 56.608 | 44.2167 | 19.3867 | 12.5603 | 8.1869 | 5.7155 | 5.5108 | 10.1237 | 17.0754 | 20.9374 | 16.0735 | 17.5217 | 12.3834 | 7.1699 | 5.1612 | 4.473 | 1.7947 | 1.4264 | 1.3109 | 5.0724 | 18.5588 | 35.6759 | 75.9716 | 35.2942 | 47.9339 | 52.2103 | 15.6596 | 10.024
Qbestfit | 13.7439 | 8.7175 | 5.1002 | 3.4972 | 9.9464 | 83.78 | 56.5923 | 88.44 | 64.699 | 48.1455 | 33.92 | 24.711 | 17.3616 | 10.6766 | 6.5846 | 6.6823 | 16.5781 | 27.543 | 47.1258 | 37.5742 | 33.1203 | 27.5474 | 20.5993 | 14.3948 | 9.4392 | 5.8814 | 3.6171 | 8.2173 | 12.4426 | 30.653 | 40.8235 | 53.3045 | 47.8163 | 43.7942 | 29.2177 | 21.0677 | 14.3406 | 8.9913 | 5.8118 | 3.4642 | 7.3313 | 23.5144 | 23.2577 | 24.7029 | 31.0133 | 24.1597 | 16.894 | 11.7109 | 7.422 | 4.872 | 2.4613 | 1.1717 | 14.689 | 24.027 | 65.2068 | 43.74 | 42.2737 | 39.1958 | 28.0873 | 20.3735
Monthly streamflow of observed and simulated discharge for validation period (2015-2019)
Results and Discussion (Contd.)
Chart: Discharge, cumec
Monthly streamflow of observed and simulated discharge for calibration period (2005-2014)

## Slide 25
Chart: Observed discharge, cumecs
 | 0 | 900
Goodness of fit between observed and simulated daily streamflow during calibration period (2005–2014)
Chart: Observed
 | 0 | 1000
Goodness of fit between observed and simulated daily streamflow during validation period (2015–2019)
Results and Discussion (Contd.)

## Slide 26
Uncertainty Parameter | Calibration (2005-2014) | Validation (2015-2019)
p-factor | 0.87 | 0.83
r-factor | 0.84 | 0.89
p-factor and r-factor of SWAT simulation in Dudhnai watershed
Uncertainty analysis
The p factor is the fraction of measured data (plus its error) bracketed by the 95PPU band. The r factor is the ratio of the average width of the uncertainty band over the standard deviation of the observed variable.
p-factor range from 0-1, in which, p-factor close to unity is desirable. While r-factor range from 0 to any real number, in which, r-factor close to 0 is desirable.
Results and Discussion (Contd.)

## Slide 27
+ c+…=

## Slide 28
Chart: Discharge, cumec
Chart: Discharge, cumec
95 percent prediction uncertainty (95ppu) plot, observed discharge and best fit simulated discharge during calibration period (2005-2014)
95 percent prediction uncertainty (95ppu) plot, observed discharge and best fit simulated discharge during validation period (2015-2019)
Results and Discussion (Contd.)

## Slide 29
Parameter Name | Minimum | Maximum | Calibrated parameter value
CN2.mgt | -0.3891 | 0.0038 | -0.2915
ALPHA_BF.gw | 0.3340 | 1.0000 | 0.8590
GW_DELAY.gw | 0.0000 | 270.9827 | 86.2628
GWQMN.gw | 771.2238 | 2315.4429 | 830.4188
ESCO.hru | 0.6006 | 0.8603 | 0.6487
SOL_AWC(..).sol | -0.0118 | 0.3651 | 0.0065
SOL_K(..).sol | -0.0566 | 0.4306 | 0.0303
CH_N2.rte | 0.1489 | 0.3000 | 0.1824
CH_K2.rte | 29.5850 | 109.9150 | 105.2290
GW_REVAP.gw | 0.0681 | 0.1645 | 0.1258
REVAPMN.gw | 126.9777 | 381.3557 | 255.4386
ALPHA_BNK.rte | 0.4006 | 1.0000 | 0.9870
OV_N.hru | 0.1296 | 0.3689 | 0.2584
SLSOIL.hru | 22.0922 | 107.4078 | 88.7806
SURLAG.bsn | 0.0500 | 2.7200 | 0.7308
Calibrated SWAT model parameters in the Dudhnai watershed
Chart: mm of water
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Direct Runoff | 0.162 | 0.65867 | 4.484 | 48.862 | 72.0327 | 181.41 | 124.156 | 127.8673 | 87.23 | 34.27 | 0.0086667 | 0.0073333
Baseflow | 5.4807 | 0.46933 | 0.16267 | 8.9327 | 45.3327 | 92.652 | 147.8173 | 163.5067 | 149.5747 | 123.4233 | 70.4353 | 31.6647
Water Yield | 9.142 | 3.8167 | 7.8633 | 69.0787 | 135.6293 | 299.964 | 300.882 | 316.412 | 258.588 | 171.9127 | 76.9873 | 36.3187
Monthly variation of direct runoff, baseflow and water yield in Dudhnai watershed
Results and Discussion (Contd.)

## Slide 30
Month | Rainfall | Direct Runoff | Lateral Flow | Baseflow | ET | Water Yield
Jan | 6.41 | 0.16 | 0.12 | 5.48 | 12.90 | 9.14
Feb | 17.13 | 0.66 | 0.37 | 0.47 | 17.47 | 3.82
Mar | 65.40 | 4.48 | 1.33 | 0.16 | 47.51 | 7.86
Apr | 260.34 | 48.86 | 9.79 | 8.93 | 100.15 | 69.08
May | 334.46 | 72.03 | 16.51 | 45.33 | 98.05 | 135.63
Jun | 493.18 | 181.41 | 23.07 | 92.65 | 74.60 | 299.96
Jul | 415.88 | 124.16 | 24.58 | 147.82 | 66.76 | 300.88
Aug | 369.39 | 127.87 | 19.58 | 163.51 | 67.40 | 316.41
Sep | 273.63 | 87.23 | 15.79 | 149.57 | 64.77 | 258.59
Oct | 117.02 | 34.27 | 7.85 | 123.42 | 52.27 | 171.91
Nov | 6.49 | 0.01 | 1.26 | 70.44 | 23.92 | 76.99
Dec | 2.79 | 0.01 | 0.29 | 31.66 | 12.66 | 36.32
Total | 2362.13 | 681.15 | 120.53 | 839.45 | 638.47 | 1686.59
Average monthly water balance components in mm in the Dudhnai watershed
1 JJAS - Months of June, July, August and September;
2 ON - Months of October and November;
3 DJF - Months of December, January and February;
4 MAM - Months of March, April and May
Average season wise water balance components in mm in the Dudhnai watershed
Results and Discussion (Contd.)

## Slide 31: Conclusions
The study area experienced an excess rainfall of 1070 mm in 2015 and a deficit of 700 mm in 2006 which implies huge variation of precipitation in the area.
73% of precipitation is converted to streamflow out of which 54% is surface runoff and rest of the streamflow are lateral and baseflow.
Curve number (CN2) and channel hydraulic conductivity (CH_K2) are the most sensitive parameters.

## Slide 32
Conclusions
NSE and value are 0.54 and 0.55 for daily time step, 0.7 and 0.72 for monthly time step respectively.
Daily observed discharge was 19.08 cumecs whereas daily simulated discharge was 20.93 cumecs, slightly overestimated result by the model.
P factor for calibration and validation period were 0.87 and 0.83 respectively, however r factor for the same were 0.84 and 0.89 respectively.
The values of the model performance indicators and uncertainties analysis of the SWAT model were satisfactory and indicated strong applicability of the model in the area.

## Slide 33: Hydrological Modelling of Pare watershed using SWAT

## Slide 34: Climate scenarios
Observed | Climate Models | Future time periods | RCPs
Pare watershed | 1. ACCESS1-0 | 1. 2023-2030 | 4.5
1. Calibration: 1991-1997 | 2. CCSM4 | 2. 2053-2060 | 8.5
2. Validation: 2003-2005 | 3. CNRM-CM5 | 3. 2083-2090 | 
Dudhnai watershed | 4. MPI-ESM-LR |  | 
Calibration: 2005-2014 Validation: 2015-2019 | 5. NorESM1-M |  | 
Scenarios 1 to 15 ~~ RCP 4.5 with 5 climate models and three distinct time periods
Scenarios 16 to 30 ~~ RCP 8.5 with 5 climate models and three distinct time periods

## Slide 35: Average temperature and precipitation in Pare watershed

## Slide 36: SWAT Modelling in Pare watershed (Model Performance)
Evaluation Parameter | Calibration (1991-1997) |  | Validation (2003-2005) | 
 | Daily | Monthly | Daily | Monthly
p-factor | 0.76 | - | 0.88 | -
r-factor | 1.19 | - | 1.07 | -
Nash-Sutcliffe Efficiency (NSE) | 0.52 | 0.72 | 0.60 | 0.78
Coefficient of Determination (R2) | 0.61 | 0.80 | 0.61 | 0.82
Coefficient of Residual Mass (CRM) | 0.17 | 0.17 | 0.02 | 0.02
Standard Error of Estimate (SEE) | 38.50 | 25.54 | 36.17 | 21.26
Percent Bias (PBIAS) | 17.3 | - | 1.6 | -
MeanSimulated(MeanObserved) | 55.94(67.67) | - | 50.99(51.80) | -

## Slide 37: SWAT Modelling in Pare watershed (Sensitivity Analysis)
Parameter Name | t-Stat | P-Value | Rank
CH_K2.rte | 41.601 | 0.000 | 1
CN2.mgt | -39.509 | 0.000 | 2
ALPHA_BNK.rte | -13.813 | 0.000 | 3
GWQMN.gw | -1.712 | 0.087 | 4
GW_REVAP.gw | -1.514 | 0.130 | 5
REVAPMN.gw | -1.061 | 0.289 | 6
SOL_K(..).sol | -0.730 | 0.466 | 7
ALPHA_BF.gw | -0.677 | 0.498 | 8
ESCO.hru | -0.428 | 0.669 | 9
GW_DELAY.gw | -0.156 | 0.876 | 10
CH_N2.rte | -0.154 | 0.877 | 11
SOL_AWC(..).sol | -0.048 | 0.962 | 12

## Slide 38: SWAT Calibration in Pare watershed (Best fit parameters)
S.No. | Parameter Name | Minimum | Maximum | Fitted Value
1 | CN2.mgt | -0.2 | 0.2 | -0.10
2 | ALPHA_BF.gw | 0 | 1 | 0.40
3 | GW_DELAY.gw | 5 | 450 | 17.68
4 | GWQMN.gw | 0 | 2000 | 315.00
5 | ESCO.hru | 0.7 | 0.99 | 0.87
6 | SOL_AWC(..).sol | -0.2 | 0.2 | 0.01
7 | SOL_K(..).sol | -0.3 | 0.3 | 0.00
8 | CH_N2.rte | 0.05 | 0.3 | 0.09
9 | CH_K2.rte | 0 | 150 | 142.13
10 | GW_REVAP.gw | 0.02 | 0.2 | 0.04
11 | REVAPMN.gw | 0 | 500 | 433.25
12 | ALPHA_BNK.rte | 0 | 1 | 0.12

## Slide 39: SWAT Calibration in Pare watershed (95PPU)
Chart: Discharge, cumec

## Slide 40: SWAT Calibration in Pare watershed (Observed vs Best fit)
Chart: Discharge, cumec
Chart: Observed Discharge, cumec
 | 0 | 800
Chart: Discharge, cumec

## Slide 41: SWAT Validation in Pare watershed (Observed vs Best fit)
Chart: Discharge, cumec
Chart: Observed Discharge, cumec
 | 0 | 500
Chart: Discharge, cumec
Rainfall | 14.2867 | 42.4233 | 100.9267 | 140.42 | 288.1933 | 462.0433 | 646.2633 | 570.71 | 424.95 | 251.33 | 30.9067 | 6.5233 | 34.3667 | 38.7233 | 171.8767 | 217.2167 | 684.8533 | 390.17 | 476.8833 | 459.15 | 309.6767 | 310.77 | 2.66 | 36.66 | 47.1267 | 102.5333 | 170.23 | 227.89 | 297.43 | 494.4567 | 468.9 | 602.7167 | 157.7967 | 88.98 | 21.4067 | 0
Qobs | 10.129 | 9.5357 | 9.3871 | 9.5333 | 14.7742 | 73 | 136.2258 | 119.3548 | 99.4 | 72.1935 | 32.7 | 19.7419 | 15.5161 | 12.3448 | 11.0645 | 34.5333 | 67.9677 | 101.2 | 159.3871 | 71.3226 | 100.5667 | 74.9355 | 23.4667 | 14.6452 | 12.0323 | 10.9286 | 13.2903 | 15.3 | 27.2258 | 48.1 | 85.7419 | 145.6452 | 110.8667 | 55.9677 | 23.4333 | 14.5161
Qbestfit | 16.6323 | 13.8721 | 13.7613 | 12.087 | 17.8497 | 39.385 | 89.2787 | 102.4816 | 100.052 | 90.0116 | 48.861 | 32.5655 | 25.5735 | 21.6917 | 21.6665 | 24.3403 | 79.761 | 72.4073 | 94.3265 | 94.5619 | 87.2753 | 87.0113 | 43.449 | 30.6148 | 25.431 | 25.1571 | 21.9632 | 25.195 | 33.7316 | 70.7937 | 86.9661 | 107.5077 | 67.4503 | 48.0177 | 31.116 | 25.1048

## Slide 42: Future water yields in Pare watershed
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5

## Slide 43: Future water yields in Pare watershed
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5

## Slide 44: Future water yields in Pare watershed
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5

## Slide 45: Future water yields in Pare watershed
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5

## Slide 46: Future water yields in Pare watershed
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5
Chart: RCP 4.5
Chart: RCP 8.5